## Slide 1: Message Queuing Telemetry Transport (MQTT)
Khamdamboy Urunov, a Ph.D. student. Special Communication Research Center., Graduate School of Financial Information Security., Kookmin University Seoul, South Korea

## Slide 2: MQTT base architecture
Publisher and subscriber
  Publisher publish (topic, info)
  Subscriber  subscribe (topic)

## Slide 3: MQTT base architecture (cont…)
Million of subscribers
Million of publisher

## Slide 4: MQTT Topic

## Slide 5: MQTT info and main parameters
http://m2mcloud.blogspot.kr/
Infrastructure in MQTT has three parts: * Broker Server. Basically, its job is to accept subscribers and re-transmit info from publisher to subscribers. In complex system, broker server can do more jobs related to data analysis and mining. * Subscriber Client. In most of time, it listens to broker after subscribing and ready for handling incoming message. * Publisher Client. In "Internet of Things" system, each device connected has the ability of sensor and can be triggered by events, which produces useful and important information to notify outside. If subscriber and publisher are both integrated in an app, then it can work in duplex mode, which can listen to and notify outside.
Obviously, MQTT is built on TCP/IP and implement Publisher-Broker-Subscriber pattern.
It means one publisher can easily achieve multicast functionality.

## Slide 6: PubSub support Broadcast 1 – to- many
MQTT Data Distribution
publisher
subscriber
Br
topic
PubSub support 1 – to- 1
publisher
Br
topic
PubSub support 1 – to- zero

## Slide 7: Open source code implementations MQTT & CoAP
MQTT
Community website
Specification
Open source implementations:
  Paho
  Mosquitto
  GitHub
Standards working group
http://www.eclipse.org/community/eclipse_newsletter/2014/february/article2.php
CoAP
IP for Smart Objects Alliance
Specification
Open source implementations:
  SourceForge
  GitHub
  Contiki
Browser plugin
REST
Standards working group

## Slide 8: MQTT Message format
MQTT V3.1 Protocol Specification
Fixed header
  Message Type
  Flags
  Remaining Length
Variable header
  Protocol name
  Protocol version
  Connect flags
  Clean session flag
  Will flag
  Will QoS
  Will Retain flag
  User name and password flags
  Keep Alive timer
  Connect return code
  Topic name
Payload
Message identifier
MQTT and UTF-8
Unused bits
CONNECT
CONNACK
PUBLISH
PUBACK
PUBREC
PUBREL
PUBCOMP
SUBSCRIBE
SUBACK
UNSUBSCRIBE
UNSUBACK
PINGREC
PINGREST
DISCONNECT
  Command Message
Variable header
Fixed header
Response
Payload
Actions
Functions:

## Slide 9: MQTT protocol details - Header
Fixed header
  Message Type
  Flags
  Remaining Length

## Slide 10
MQTT protocol details – Header (cont…)
Flags
The remaining bits of byte 1 contain the fields DUP, QoS, and RETAIN. The bit positions are encoded to represent the flags as shown in the table below.

## Slide 11: MQTT Message format
Message | 4- bit code | Description
CONNECT | 1 | Client request to connect to Server
CONNACK | 2 | Connect Acknowledgment
PUBLISH | 3 | Publish message
PUBACK | 4 | Publish Acknowledgment
PUBREC | 5 | Publish Received (assured delivery part1)
PUBREL | 6 | Publish Release (assured delivery part 2)
PUBCOMP | 7 | Publish Complete (assured delivery part 3 )
SUBSCRIBE | 8 | Client Subscribe request
SUBACK | 9 | Subscribe Acknowledgment
UNSUBSCRIBE | 10 | Client Unsubscribe request
UNSUBACK | 11 | Unsubscribe Acknowledgment
PINGREC | 12 | PING Request
PINGREST | 13 | PING Response
DISCONNECT | 14 | Client is Disconnecting
Reserved | 15 | Reserved
4- bit code | Represented as a 4-bit unsigned value. The version of the protocol
Message type:

## Slide 12: MQTT Control Packet format
Fixed header
Fixed header
  Message Type
  Flags
  Remaining Length
The message header for each MQTT command message contains a fixed header. The table below shows the fixed header format.
Byte 1
Contains the Message Type and Flags (DUP, QoS level, and RETAIN) fields.
Byte 2
(At least one byte) contains the Remaining Length field. The fields are described in the following sections.
All data values are in big-endian order: higher order bytes precede lower order bytes.
A 16-bit word is presented on the wire as Most Significant Byte (MSB), followed by Least Significant Byte (LSB).

## Slide 13
MQTT Control Packet format (cont…)
Position: byte 1, bits 7-4
The enumerations for this version of the protocol are shown in the table below.
Fixed header
  Message Type
  Flags
  Remaining Length

## Slide 14
MQTT Control Packet format (cont…)
Fixed header
  Message Type
  Flags
  Remaining Length
The remaining bits of byte 1 contain the fields DUP, QoS, and RETAIN. The bit positions are encoded to represent the flags as shown in the table below.
DUP
Position: byte 1, bit 3.
This flag is set when the client or server attempts to re-deliver a PUBLISH, PUBREL, SUBSCRIBE or UNSUBSCRIBE message
This applies to messages where the value of QoS is greater than zero (0), and an acknowledgment is required.
When the DUP bit is set, the variable header includes a Message ID.
The recipient should treat this flag as a hint as to
whether the message may have been previously received. It should not be relied on to detect duplicates.

## Slide 15
MQTT Control Packet format (cont…)
Fixed header
  Message Type
  Flags
  Remaining Length

## Slide 16
Position: starts at byte 2.
The Remaining Length is the number of bytes remaining within the current packet,
including data in the variable header and the payload.
The Remaining Length does not include the bytes used to encode the Remaining Length.
The Remaining Length is encoded using a variable length encoding scheme which uses a single byte for values up to 127
Larger values are handled as follows.
The least significant seven bits of each byte encode the data, and the most significant bit is used to indicate that there are following bytes in the representation.
Thus each byte encodes 128 values and a "continuation bit". The maximum number of bytes in the Remaining Length field is four.
Non normative comment.
For example, the number 64 decimal is encoded as a single byte, decimal value 64, hexadecimal 0x40.
The number 321 decimal (= 65 + 2*128) is encoded as two bytes, least significant first.
The first byte 65+128 = 193. Note that the top bit is set to indicate at least one following byte. The second byte is 2.
MQTT Control Packet format (cont…)
Fixed header
  Message Type
  Flags
  Remaining Length

## Slide 17
Non normative comment.
This allows applications to send Control Packets of size up to 268,435,455 (256 MB).
The representation of this number on the wire is: 0xFF, 0xFF, 0xFF, 0x7F.
The table below shows the Remaining Length values represented by increasing numbers of bytes.
MQTT Control Packet format (cont…)
Fixed header
  Message Type
  Flags
  Remaining Length

## Slide 18
MQTT message format

## Slide 19
MQTT message format (cont…)

## Slide 20
RETAIN (keep last message):
RETAIN=1 in a PUBLISH message instructs the server to keep the message for this topic.
When a new client subscribes to the topic, the server sends the retained message.
Typical application scenarios:
Clients publish only changes in data, so subscribers receive the last known good value.
MQTT message format (cont…)
Example: Subscribers receive last known temperature value from the temperature data topic. RETAIN=1 indicates to subscriber B that the message may have been published some time ago

## Slide 21
MQTT message format (cont…)

## Slide 22: CONNECT message format:
MQTT message format (cont…)
The CONNECT message contains many session-related information as optional header fields.
CONNECT | 1 | Client request to connect to Server

## Slide 23
Overview CONNECT message fields:
MQTT message format (cont…)

## Slide 24
CONNACK message format:
MQTT message format (cont…)
CONNACK | 2 | Connect Acknowledgment

## Slide 25
MQTT message format (cont…)
PUBLISH | 3 | Publish message

## Slide 26
MQTT message format (cont…)
PUBACK | 4 | Publish Acknowledgment
PUBREC | 5 | Publish Received (assured delivery part1)

## Slide 27
MQTT message format (cont…)
PUBREL | 6 | Publish Release (assured delivery part 2)
PUBCOMP | 7 | Publish Complete (assured delivery part 3 )

## Slide 28
MQTT message format (cont…)
SUBSCRIBE | 8 | Client Subscribe request

## Slide 29
MQTT message format (cont…)
SUBACK | 9 | Subscribe Acknowledgment

## Slide 30
MQTT message format (cont…)
UNSUBSCRIBE | 10 | Client Unsubscribe request

## Slide 31
MQTT message format (cont…)
UNSUBACK | 11 | Unsubscribe Acknowledgment
PINGREC | 12 | PING Request
PINGREST | 13 | PING Response
DISCONNECT | 14 | Client is Disconnecting
http://www.slideshare.net/PeterREgli/mq-telemetry-transport

## Slide 32
MQTT QoS value
http://www.slideshare.net/PeterREgli/mq-telemetry-transport

## Slide 33
MQTT QoS value (cont…)

## Slide 34: MQTT QoS value (cont…)
http://www.slideshare.net/ragupta2/mqtt-a-protocol-for-the-internet-of-things

## Slide 35: MQTT QoS value (cont….)
http://www.slideshare.net/paolopat/mqtt-iot-protocols-comparison
  "At most once", where messages are delivered according to the best efforts of the underlying TCP/IP network.
  Message loss or duplication can occur.
  This level could be used, for example, with ambient sensor data where it does not matter if an individual reading is lost as the next one will be published soon after.

## Slide 36
http://www.slideshare.net/paolopat/mqtt-iot-protocols-comparison
"At least once", where messages are assured to arrive but duplicates may occur.
MQTT QoS value (cont…)

## Slide 37
http://www.slideshare.net/paolopat/mqtt-iot-protocols-comparison
  "Exactly once", where message are assured to arrive exactly once.
  This level could be used, for example, with billing systems where duplicate or lost messages could lead to incorrect charges being applied.
MQTT QoS value (cont…)

## Slide 38
MQTT QoS value (cont…)

## Slide 39
MQTT QoS value (cont…)

## Slide 40: MQTT CONNECT and SUBSCRIBE message sequence

## Slide 41
MQTT CONNECT and SUBSCRIBE message sequence (cont…)

## Slide 42: MQTT Client Comparison
http://www.eclipse.org/paho/downloads.php

## Slide 43: MQTT Experimental
http://www.eclipse.org/paho/downloads.php

## Slide 44: MQTT Stable
http://www.eclipse.org/paho/downloads.php

## Slide 45
Thank you!
hamdamboy.urunov@gmal.com